## Slide 1
SnoozeGuard
Prototype Development of an AI-Driven
Real-Time Drowsiness Monitoring System for Road Safety
Cart Jeuiel T. Agno · Aira Mae T. Pilor · Christian Eduard B. Ylagan Jr.
Research Adviser: Engr. Jezer E. Ilao
Divine Word College of Calapan · School of Engineering · BS Computer Engineering · 2025–2026

## Slide 2
Presentation Outline
01
Background & Problem
02
Objectives of the Study
03
System Overview
04
Detection Algorithm
05
Alert Escalation System
06
IoT Alert Device
07
Emergency Notification
08
Methodology & Evaluation
09
Results & Conclusions

## Slide 3
Background
Drowsy driving contributes to ~20% of all motorway accidents (Horne & Reyner, 1995)
WHO (2023): road traffic injuries are the 8th leading cause of death globally
Microsleep episodes (3–30 seconds) cause vehicles to travel 100+ meters uncontrolled
Commercial Driver Monitoring Systems (DMS) are prohibitively expensive for most drivers
Smartphone-based detection offers an accessible, vehicle-agnostic alternative
No existing low-cost system combines multi-signal detection + IoT alerts + emergency notification

## Slide 4
Statement of the Problem
1
How can a smartphone reliably detect drowsiness using multiple physiological signals (yawn, head nod, tilt, brake)?
2
How can drowsiness severity be quantified into a 10-level model driving proportional alert responses?
3
How can a low-cost IoT device augment alerts with audio, vibration, and LED patterns per level?
4
How can an emergency pipeline reliably notify a guardian even under intermittent connectivity?
5
To what extent does SnoozeGuard meet ISO/IEC 25010 software quality requirements?

## Slide 5
Objectives of the Study
General Objective
To design, develop, and evaluate SnoozeGuard — a multi-platform AI-driven real-time drowsiness monitoring system — capable of detecting driver fatigue, delivering graduated alerts, and triggering emergency contact notifications at critical levels.
Specific Objectives
Implement multi-signal detection: yawn (jawOpen blend shape), head nod (pitch/roll), sustained tilt (10s), sudden brake (accelerometer)
Develop a configurable 10-level drowsiness scoring model with administrator-controlled thresholds
Build an ESP32 IoT alert device with MQTT + BLE communication and level-specific audio/vibration/LED patterns
Implement an emergency notification pipeline via Expo Push + PhilSMS SMS to the active emergency contact
Implement an offline-first SQLite architecture with automatic Supabase cloud synchronization
Evaluate the system against ISO/IEC 25010 across 8 quality characteristics

## Slide 6
System Architecture Overview
Mobile App
(React Native / Expo SDK 54)
Web Dashboard
(React + Vite / Firebase)
IoT Alert Device
(ESP32 + DFPlayer Mini)
IoT API + MQTT Bridge
(Node.js / Hono / Railway)
Supabase Cloud Backend (PostgreSQL · Auth · Realtime · Edge Functions)
MQTT Broker — HiveMQ Cloud TLS 8883
SMS — PhilSMS via Supabase Edge Function
Push Notifications — Expo Push (APNs / FCM)
Deployment
Mobile
Expo EAS (expo.dev)
Web
Firebase Hosting
API
Railway
Backend
Supabase
MQTT
HiveMQ Cloud
SMS
PhilSMS

## Slide 7
Drowsiness Detection Algorithm
MediaPipe Face Landmarker
478 facial landmarks + 52 blend shape coefficients · Mobile: IMAGE mode @ 600ms · Web: VIDEO mode @ 130ms (WASM)
Yawn Detection
jawOpen blend shape ≥ 0.70 → open
jawOpen ≤ 0.40 → yawn confirmed
Cooldown: 2,000ms
Head Nodding
Pitch > 0.35 or Roll > 0.25 rad
Fires on centered→offCenter transition
Cooldown: 500ms
Sustained Tilt
Off-center for ≥ 10 seconds
(4 grace frames allowed)
→ Independent Level 8 alert modal
Sudden Brake
Accelerometer delta > 0.45 g
2 qualifying events within 3,000ms
→ Independent brake alert modal
Drowsiness Level Computation
computeLevelFromAlertMap( yawnAcc, headAcc, alertMap ) → Level 0–10
For each level 1→10: if yawnAcc ≥ threshold OR headAcc ≥ threshold → set computedLevel. Returns highest matched level. Thresholds are administrator-configurable via Admin Config screen.

## Slide 8
Alert Escalation System
Levels 1–2
Very Low / Low
Voice warning
Levels 3–4
Mild / Moderate
Voice + Vibration
Level 5
Moderate-High
Voice + Vibration + Alarm
Levels 6–8
High / Severe
Voice + Vibration + Alarm + IoT Device
Levels 9–10
Critical / Extreme
All above + Emergency Notification (120s timer)
Dismiss Guard: dismissedLevelsRef prevents same level re-firing per session · Level 10 re-triggers after 3 more yawns or 10 more head events

## Slide 9
IoT Alert Device — ESP32
Hardware Components
ESP32 DevKit — WiFi + BLE + GPIO (240MHz dual-core)
DFPlayer Mini — UART2 (GPIO 16/17) — plays 0001–0005.mp3 from MicroSD
Buzzer (GPIO 26) · LED Primary (GPIO 27) · LED Secondary (GPIO 32) · BLE LED (GPIO 33)
Dismiss Button — GPIO 25, INPUT_PULLUP, 200ms debounce
Alert Behavior by Level
Level | MP3 Track | Vibration Pattern | LED
6 | 0001.mp3 | 3 short pulses (200ms on / 150ms off) | Pulsed
7 | 0002.mp3 | 3 medium pulses (400ms on / 150ms off) | Pulsed
8 | 0003.mp3 | 3 long pulses (600ms on / 150ms off) | Pulsed
9 | 0004.mp3 | Continuous buzzer | Continuous on
10 | 0005.mp3 | Continuous buzzer | Flashing (400ms on/off)
Dismiss button → MQTT publish snoozeguard/dismiss/{device_id} + BLE NOTIFY {event:dismiss} → server updates iot_alerts.status → Supabase Realtime → mobile dismiss

## Slide 10
IoT Connectivity & Communication
Mobile App
(React Native)
HiveMQ Cloud
MQTT TLS :8883
ESP32
IoT Device
POST /v1/iot/buzz →
MQTT publish
snoozeguard/commands/{id}
BLE Fallback (SG-{device_id}) CMD char: beb5483e-... EVENT char: beb5483f-...
Topic Structure
App → Device
snoozeguard/commands/{device_id}
buzz / all_clear JSON command
Device → Server
snoozeguard/dismiss/{device_id}
dismiss event from physical button
Device → Server
snoozeguard/ping/{device_id}
heartbeat every 5s → updates last_seen
Device online if last_seen < 15s · BLE used when WiFi/MQTT unavailable

## Slide 11
Emergency Notification System
1
Driver reaches Level 9 or 10 — alert modal opens
2
120-second countdown begins (30s on web)
3
If driver does NOT dismiss → triggerEmergencyAlert() fires
4
Driver's GPS location captured → emergency_alert_events row inserted
5
Expo Push Notification sent to active emergency contact's device
6
If sms_enabled: POST to Supabase Edge Function → PhilSMS API → SMS delivered
7
Guardian opens EmergencyAlertMapScreen → sees live location → Accept / Dismiss
Multi-contact model: driver designates multiple guardians (is_active=1 selects active). Real-time presence shown in "I Protect" tab.

## Slide 12
Offline-First Architecture
Local SQLite (expo-sqlite)
Ground Truth — Always Available
Background
Sync
Supabase PostgreSQL
Cloud Backup
Offline-First Pattern
Read SQLite immediately
Show cached data to user with zero delay
Check connectivity
isOnline() from sync/flush.ts
If online: fetch Supabase
Update SQLite cache with fresh data
If offline: show banner
User sees offline warning; cached data still visible
Auth Fallback
5-second timeout on session load → reads offline_session from SQLite → user logged in without network

## Slide 13
Research Methodology
Iterative Software Development Life Cycle (Iterative SDLC)
Phase 1
Requirements
Analysis
Jan 1–15
Phase 2
System
Design
Jan 16–30
Phase 3
Mobile App
Development
Feb 1–15
Phase 4
Web Dashboard
Feb 16–28
Phase 5
IoT Firmware
Mar 1–15
Phase 6
Integration
Testing
Mar 16–30
Phase 7
Evaluation
& Survey
Apr 1–15
Phase 8
Documentation
Apr 16–30
Evaluation Framework — ISO/IEC 25010
Functional Suitability
Performance Efficiency
Compatibility
Usability
Reliability
Security
Maintainability
Portability
Respondents
Active drivers · Age: 22–35 years old · Purposive sampling · Evaluated using the driving simulator prototype
Method: 5-point Likert Scale → Weighted Mean → Interpretation (Poor / Fair / Good / Very Good / Excellent)

## Slide 14
Driving Simulator Prototype
To provide a realistic, controlled evaluation environment without requiring road access, the research team constructed a physical driving simulator:
Car Seat
Genuine automobile bucket seat on rigid wooden frame — authentic driving posture and camera distance
Steering Wheel
Logitech gaming steering wheel with force feedback at ergonomic height
Pedals
Brake and accelerator pedals at floor level — natural foot position for test participants
Smartphone Mount
Front-facing dash cradle at 60–80 cm — camera captures full face within MediaPipe range
Frame
Dimensional lumber (2×4, 2×6) — structural rigidity and adjustability
All respondents interacted with the system through this simulator before completing the ISO/IEC 25010 evaluation questionnaire

## Slide 15
Results & Discussion — ISO/IEC 25010
Quality Characteristic | Weighted Mean | Interpretation
Functional Suitability | 4.05 | Very Satisfactory
Performance Efficiency | 4.11 | Very Satisfactory
Compatibility | 4.02 | Very Satisfactory
Usability | 3.90 | Very Satisfactory
Reliability | 3.91 | Very Satisfactory
Security | 4.04 | Very Satisfactory
Maintainability | 3.98 | Very Satisfactory
Portability | 4.07 | Very Satisfactory
Grand Mean (n = 29) | 4.01 | Very Satisfactory
All 8 characteristics rated Very Satisfactory. Highest: Performance Efficiency (4.11). Lowest: Usability (3.90).

## Slide 16
Conclusions
1
A smartphone camera + MediaPipe Face Landmarker can reliably detect multi-signal driver drowsiness (yawn, head nod, tilt, brake) in real time without specialized vehicle hardware.
2
A configurable 10-level drowsiness scoring model provides proportional, escalating alert responses that avoid the false-alarm fatigue of binary threshold systems.
3
An ESP32 IoT alert device with MQTT + BLE dual-path communication successfully extends alerts beyond the smartphone with level-calibrated audio, vibration, and LED patterns.
4
A closed-loop emergency pipeline (Expo Push + PhilSMS) delivers timely guardian notification absent from existing smartphone DMS applications.
5
An offline-first SQLite architecture ensures continuous session recording under intermittent network conditions — critical for Philippine road environments.
6
SnoozeGuard achieves [pending ISO score] across ISO/IEC 25010 quality characteristics — demonstrating satisfactory software quality as a functional prototype.

## Slide 17
Recommendations
Field Validation
Evaluate in naturalistic driving conditions across diverse road types, lighting, and driver demographics
Eye Closure Integration
Add PERCLOS as optional supplementary signal when MediaPipe reports high-confidence eye landmark tracking
OBD-II Integration
Incorporate vehicle speed and lane deviation data as additional drowsiness signals
Regulatory Certification
Pursue formal safety analysis and certification pathway for deployment as a certified DMS aid
Multi-Language Support
Add Filipino TTS and localized UI for broader Philippine deployment
Fleet Management Dashboard
Extend cloud backend to aggregate driver drowsiness statistics across commercial vehicle fleets
Battery Optimization
Investigate adaptive sampling and Android NNAPI hardware acceleration to reduce power consumption

## Slide 18
Thank You
Questions & Open Discussion
Cart Jeuiel T. Agno · Aira Mae T. Pilor · Christian Eduard B. Ylagan Jr.
Adviser: Engr. Jezer E. Ilao · Divine Word College of Calapan · BS Computer Engineering · 2025–2026