## Slide 1
DIVINE WORD COLLEGE OF CALAPAN · School of Engineering · BS Computer Engineering
SnoozeGuard
AI-Driven Real-Time Driver Drowsiness
Monitoring & Alert System
Prototype Development for Road Safety
WHAT IS SNOOZEGUARD?
SnoozeGuard is a multi-platform AI system that uses your smartphone's front camera and Google's MediaPipe to detect drowsiness in real time while driving — without any vehicle modification.
HOW IT DETECTS DROWSINESS
😮
Yawn Detection
jawOpen blend shape ≥ 0.70
😴
Head Nodding
Pitch/Roll threshold breach
↗️
Sustained Tilt
10 seconds off-center
🛑
Sudden Brake
Accelerometer delta > 0.45g
10-LEVEL ALERT ESCALATION
Level 1–2
Voice
Level 3–5
Voice + Vibration
+ Alarm
Level 6–8
All above
+ IoT Device
Level 9–10
All above
+ Emergency SMS
📡 ESP32 IoT Alert Device · MQTT HiveMQ TLS · BLE Fallback · DFPlayer MP3 · Physical Dismiss Button
BUILT WITH
React Native
MediaPipe
Supabase
ESP32
HiveMQ MQTT
PhilSMS
Firebase
Railway
RESEARCHERS
Cart Jeuiel T. Agno · Aira Mae T. Pilor · Christian Eduard B. Ylagan Jr.
Research Adviser: Engr. Jezer E. Ilao · 2025–2026

## Slide 2
SnoozeGuard
HOW IT WORKS
01
Camera Captures Face
The smartphone front camera takes a snapshot every 600ms. MediaPipe Face Landmarker processes 478 facial landmarks and 52 blend shape coefficients on the device — no internet required for detection.
02
Signals Are Detected
Four drowsiness signals are extracted: yawning (jawOpen ≥ 0.70), head nodding (pitch/roll threshold), sustained head tilt (10 seconds), and sudden braking (accelerometer delta > 0.45g).
03
Drowsiness Level Computed
Yawn and head movement counts feed into a configurable 10-level scoring engine. The administrator can tune thresholds per level via the Admin Config screen.
04
Graduated Alerts Fire
Levels 1–5: Voice + vibration on the smartphone.
Levels 6–8: Additionally activates the ESP32 IoT alert device (MP3 audio, vibration pulses, LED).
Levels 9–10: All of the above + 120-second emergency countdown.
05
Emergency Notification Sent
If the driver does not dismiss the alert within 120 seconds, an Expo push notification and a PhilSMS text message are automatically sent to the driver's designated emergency contact with the driver's GPS location.
06
Guardian Responds
The emergency contact opens the SnoozeGuard app, sees the driver's live location on a map, and can acknowledge or dismiss the alert — completing the safety loop.
Cart Jeuiel T. Agno · Aira Mae T. Pilor · Christian Eduard B. Ylagan Jr. · DWCC School of Engineering · 2025–2026

## Slide 3
IoT Alert Device
ESP32-Based Physical Alert Peripheral
SnoozeGuard — Hardware Component
HARDWARE COMPONENTS
ESP32 DevKit
Dual-core 240MHz · WiFi + BLE + GPIO
DFPlayer Mini
UART2 (GPIO 16/17) · Plays 0001–0005.mp3 from MicroSD
3W Speaker
Connected to DFPlayer for audio alert output
Buzzer (GPIO 26)
Continuous or pulsed vibration alert
LED × 2 (27, 32)
Alert indicator — pulsed, continuous, or flashing
BLE LED (GPIO 33)
Bluetooth connection status indicator
Dismiss Button
GPIO 25 · INPUT_PULLUP · 200ms debounce
ALERT BEHAVIOR BY DROWSINESS LEVEL
Level
Audio
Vibration Pattern
LED
6
0001.mp3
3 short pulses (200ms on/150ms off)
Pulsed
7
0002.mp3
3 medium pulses (400ms on/150ms off)
Pulsed
8
0003.mp3
3 long pulses (600ms on/150ms off)
Pulsed
9
0004.mp3
Continuous buzzer
Continuous on
10
0005.mp3
Continuous buzzer
Flashing (400ms)
🔘 Physical Dismiss Button — Press to stop all alerts
Publishes MQTT + BLE NOTIFY → syncs dismiss state to mobile app and web dashboard
SnoozeGuard · DWCC School of Engineering · BS Computer Engineering · 2025–2026